Local Optimization

Local optimization
- Focuses on optimizing a single block
- Is simple

Some statements can be deleted
- x := x + 0
- x := x * 1

Simplify statements via algebraic manipulation
- Assignment of a constant to a variable
  x := x * 0 → x := 0
  This is not a actual optimization as multiplication is as fast as any single instruction in modern processors. But enables further optimizations through constant propogation.
- Replacing the exponentiation operation to an explicit multiply operation
  y := y2 → y = y * y
  Exponentiation is most certainly a library function with a procedure call overhead and a general loop
- Replace a multiplication by a power of two by a left shift operation
  x := x * 8 → x := x << 3
  x := x * 15 → x := x << 4; x := t -x
  This is not an optimization as multiplication is as fast as any single instruction in modern processors.

Constant folding
- Operations on constants can be computed at compile time
  - x := 2 + 2 → x := 4
  - if 2 < 0 jump L can be deleted
- Pitfall – Constant folding should not be done while cross compiling as floating point computations(due to different precisions or different strategies on rounding) may differ slightly in the compiling and target platform

Eliminate unreachable basic blocks
- An unreachable basic block is one that is not the target of any jump or fall through
- Removing unreachable block makes the code smaller and sometimes faster due to cache effects in increasing spatial locality.
- Unreachable blocks are fairly common
  - Code is parameterized with compiler time flags
  - Programs use only some interfaces offered in a large library
  - Unreachable code also occur due to other optimization

Dead code elimination

Common subexpression elimination based on single assignment form
- A block is said to be composed of single assignment forms if reassignments to the same registers are not allowed. A register can be assigned just the once.
- What this means is that if two assignments have the same RHS, the compute they same value and the duplicate computation can be saved off

  x := y + z
  …
  w := y + z

x := y + z
…
w := x

Copy propagation based on single assignment form
If w := x appears in a block, replace subsequent uses of w with x

b := z + y
a := b
x = 2 * b
b := z + y
a := b
x = 2 * a
b := z + y
x = 2 * b
Dead code elimination

Copy Propagation

By itself not useful. Enables optimization by combining with other forms of local optimization like constant folding and dead code elimination

Nature of optimizations
- Each local optimization does little by itself
- They typically interact with one another. One optimization enables another one
- Optimizing compilers repeat optimization until no improvement is possible.
- The possible combination that provides optimization with the least number of passes is copy propagation, constant propagation and constant folding

Peephole optimization
- Done directly on assembly instructions
- The peephole is a short sequence of(usually contiguous) instructions
- The optimizer replaces the peephole with a equivalent but faster sequence of instructions
- Examples :
  - move $a $b, move $b $a → move $a, $b
    Works if move $b, $a is not the target of a jump instruction
  - addiu $a $a i, addiu $a $a j → addiu $a, $a i + j
  - addiu $a $b 0 → move $a $b
  - move $a $a → delete
- As with local optimizations, peephole optimizations must be applied repeatedly for maximal effect

Strength reduction
- A variable x is said to be an induction variable if there is a positive or neagtive constant c such that each time x is assigned, its values increases by c.
- The transormation of replacing an expensive operation, such as multiplication, by a chearper one such as addition is known as strength reduction. Not only do induction variables allows us sometimes to perform a strength reduction in a loop; often it is possible to eliminate all but one of a group of induction variables whole values remain in lock step as we go around the loop.
- Consider the loop,B2, i = i + 1 newline t2 = 4 * i newline t3 = a[t2] newline if t3 < v goto B2 . After strength reduction the loop becomes, i = i + 1 newline t2 = t2 + 4 newline t3 = a[t2] newline if t3 < v goto B2 , with t2 = 4 * i, being set before entry into the loop