Register Allocation

Register allocation problem
The intermediate code uses unlimited number of registers which have to be mapped to the finite number of available registers offered by the architecture of a machine.

Solution
- Two temporaries can occupy the same register if both are not live at the same time.
- So determine the liveness information at every point in the code which will tell us the temporaries which are live at the same point of time.
- Construct a Register interference graph(RIG – Figure 17) using the liveness information of the intermediate code.
  - The RIG is a data structure used to solve the register allocation problem.
  - It is an undirected graph with each node standing for a temporary.
  - There is an edge b/w two temporaries if they are live at a same point in the program.
  - Thus two temporaries can be assigned the same registers if there is no edge connecting them.
- If a RIG is k-colorable, then there is a register assignment that uses no more than k colors. If it isn't registers are spilled.
  - This problem is NP-hard. There are no known efficient algorithms
  - We color an RIG based on the following heuristic.
    - Pick a node t with lesser than k neighbors in RIG
    - Eliminate t and all its edges from the RIG
    - If the resulting graph is k-colorable, then the original graph is colorable as t can be colored with the left-over color.
  - Implementation
    - Repeat until graph is empty
      - Pick a node t with lesser than k neighbors in RIG
      - Put t in a stack and remove it from the RIG
    - Repeat until stack is empty
      - Pop the stack and assign a color to the node that is different from its existing neighbors
      - If there isn't such a color left(there are k neighbors to the node)
        - Spill the register by allocating memory for the node to be spilled, typically in the current stack frame.
        - Modify the control flow graph by
          - inserting a load instruction before trying to read the spilled value.
          - inserting a store instruction before trying to write the spilled value.
        - The loads and the stores at each usage will have introduced new names in the code
          - Recompute the liveness of that variable. The liveness of the new name introduced at each previous use of the variable is extremely short leading to less interferences.
          - Rebuild the RIG and start over.
- The RIG can also be minimally colored with the Powell and Welsh algorithm to determine the if k number of registers are sufficient.

Performance
Note : Registers allocation is more difficult for CISC