Error detection and correction
- Parity checks
- Checksumming(Transport layer)
- Cyclic redundancy checks

Parity checks
Single bit parity checks – Cannot detect even number of errors.
Data Bits	Even Parity bit	Odd Parity bit
0111000110101011	1	0

- Two dimensional parity checks
  - Can detect and correct 1-bit errors.
  - Can only detect, but not correct, any 2 bit errors.
  - No errors - Illustration
	Data bits	Even parity bit calculated for each row
	10101 / 11110 / 01110	1 / 0 / 1
Even parity calculated for each column →	00101	0

  - Correctable single bit error
	Data bits	Even parity bit calculated for each row / Error
	10101 / 10110 / 01110	1 / 0 / 1
Even parity calculated for each column →	00101 / Error	0

Cyclic redundancy checks
D : Data bits to be sent / (d bits)	R : CRC bits / (r bits)

- The data bits, D, is shifted r positions to the left to make way for the CRC bits to be inserted, i.e., D times 2^ r XOR R is transmitted
- Calculation of the CRC bits
  - Sender and receiver use a known r + 1 long generator G.
  - R = (D times 2^r) "%" G . Now D times 2^ r XOR R is such that it is exactly divisible by G.
- Error detection
  - Error if D times 2^ r XOR R divided by G leaves a remainder