Firewalls

A combination of hardware and software that isolates a corporations internal network from the outer internet.

Packet filtering
Conceptual firewall implemented at the network layer.

Filtering decisions
- IP source of destination address
  - Not useful if attacker spoofs IP.
- TCP or UDP source or destination numbers
  - Helps filter out packets of specified application
- ICMP message type
- Other fields in TCP packets like
  - TCP SYN
  - ACK

How can only incomming(and not outgoing) TCP connections be filtered?
The first segment of a TCP connection has ACK=0. Filter for this.

Application gateway
An application gateway server through which all application specific data must pass. Multiple application gateways can run on the same host, but wach as a seperate server with its own process

Advntages of application gateways over packet filters
Finer control. Application gateways being application specific will be able to filter out by interpreting application data.

Disadvantages of application gateways
- One application gateway for every application needed.
- Performance penalty as all data must pass through AG
- Extra configuration effort of application to connect through AG.

Mapping?
Gathering info about
- IP addresses of machines in a network
- OSes
- Services run

What is IP spoofing?
Placing an incorrect IP address in the datagrams source address field to mask true asource address
Since modifying the datagram field requires modification in the network layer protocol, a user must have access to the OS code

How can spoofing be prevented?
By performing ingress filtering at routers

What is ingress filtering
Checking the IP addresses of datagrams and making sure that the source address is in the range adrresses that are known to be reachable via that interface.

Packet sniffing?
Passively recieveing all data-link layer frames passing by the devices network adapter or network card.

How can packet sniffing be done on an ethernet LAN
By setting the ethernet network adapter or card in primiscuous mode. Then the adapter/card received all passing ethernet frames

How can an interface running in primiscous mode be detected remotly?
A host that replies to an ICMP echo datagram that is correctly addressed in

Syn flooding attack
A type of Denial of service attack.
Atacker sends large amount of packets to the trageted server with spoof IP addreses and then does not complete the connection by responding to the servers 2nd handshake in the 3-handshake protocol leaving th server wasting resources it reserved for a connection

Smurf attack
Making a large number of innocent hosts respond to a ICMP echo request that contains a spoofed address. This results in a large number of echo-request-reply datagrams at the source whose address was spoofed.

What does it mean to say that a nonce is once-in-a-lifetime? In whose lifetime?
Once a server issuses a nonce, it never uses it again.

Fragment Attack
Tiny Fragment Attack is a class of attack on Internet firewalls taking advantage that it is possible to impose an unusually small fragment size on outgoing packets. If the fragment size is made small enough to force some of a TCP packet's TCP header fields into the second fragment, filter rules that specify patterns for those fields will not match. If the filtering implementation does not enforce a minimum fragment size, a disallowed packet might be passed because it didn't hit a match in the filter.