Hierarchical routing
Need for Hierarchical routing
- Scale
- Administrative authority

Autonomous systems
An autonomous system is a group of routers under a single administrative control, running the same routing protocol, the intra-AS-routing protocol.

Inter-AS routing protocol
Used to
- Obtain reachability information from neighbouring AS's
- Propagating reachability information to all internal routers of an AS

Gateway router
Routers at the edge of an AS, responsible for forwarding packets outside an AS

Hot-potato routing - Steps in adding an outside-AS destination in a routers forwarding table
- Learn from inter-AS that subnet x is reachable via multiple gateways
- Use routing info from intra-AS to determine costs of least cost to these gateways
- Hot potato routing – Choose the gateway that has the smallest least cost
- Determine from forwarding table, the interface I for that gateway. Add (x, I) in forwarding table.