ICMP(Internet control message protocol)

- Communicates network layer information between end hosts and routers. This is done through the use of control messages. Control messages can be
  - Error messages generated by intermediate routers to communicate that something is wrong with the Datagram/Network
    - Destination/Host/Port unreachable/unknown.
    - TTL expired
    - IP header bad
  - Messages other than data transmission which helps us diagnose problems
    - Echo request/reply
    - Router advertisements/discovery
- It sits above the IP and is strictly a transport layer protocol. However it serves the network layer

ICMP segment
ICMP type
ICMP code
First 20 bytes of the respective IP datagram which is responsible for the generation of this ICMP segment.

How the 'ping' app uses icmp
Sends a ICMP echo_request packet to the host

How traceroute uses icmp
Sends successive UDP packets with incremented TTL values starting from 1. Constructs the route with the