IP(v4)

IP datagram
Version / (4)	Header length in words / (4)	Type of service / (8)	Datagram length in bytes / (16)
Fragment Identifier / (16)			Flags / (3)	Fragmentation offset in double words / (13)
TTL / (8)		Upper layer protocol / (8)	Header checksum / (16)
Source IP / (32)
Destination IP / (32)
Options(Max of 11 words if any) / (32)
Data

Need for fragmentation of OP datagrams
Different link layer protocols have differenst MTU's. As a result a frame of one type of link might not fit into another.

Role of fields in the IP datagram which help in fragmentation and re-assembly
- 16-bit identifier – All fragments of a perticular datagram have the same identifier after their fragmentation by an intermediate router.
- Fragmentation offset – Helps in reassembly by indicating the relative place of a fragment within a datagram.
- Flags
  - Used to control or identify fragments. They are (in order, from high order to low order):
    - bit 0: Reserved; must be zero.
    - bit 1: Don't Fragment (DF)
    - bit 2: More Fragments (MF)
  - If the DF flag is set and fragmentation is required to route the packet then the packet is dropped. This can be used when sending packets to a host that does not have sufficient resources to handle fragmentation. It can also be used for Path MTU Discovery, either automatically by the host IP software, or manually using diagnostic tools such as ping or traceroute.
  - For unfragmented packets, the MF flag is cleared. For fragmented packets, all fragments except the last have the MF flag set. The last fragment has a non-zero Fragment Offset field, differentiating it from an unfragmented packet.
Why is reassembly not done in intermediate routers
A design decision. Router performance suffers

Classless addressing
- a.b.c.d/x, where x indicates the number of bits in the forst part of the address, thus indicating the subnet.
- A, b, c and d represent one byte of the address in decimal.

Classful addressing
a.b.c.d, The network portion of the IP address is constrined to be 8, 16 and 24 bits and these networks are known as class A, B and C networks.

Hierarchy of internet address registers
- ICANN
  - ARIN
  - RIPE
  - APNIC
  - LACNIC

Methods to assign individual IP addresses to host by Isp's or networks administrators
- Manual assignment
- Through DHCP

Types of addressing
- Unicasting – A transmission to a single interface card
- Multi-casting(1110xxxx.X.X.X) – A transmission to a group of interface cards
- Broadcasting
  - Limited broadcasting(255.255.255.255) – A transmission to all interface cards in the same network as the source
  - Directed broadcasting(AnetId.255.255.255, BnetID.255.255, CnetID.255) – A transmission to all interface cards in a particular network

Sub-netting
- An IP address can be seen as having two parts
  - The network prefix
  - The host number
- The network prefix is used by routers to route the packet to the correct destination network which might belong to some organization. The internal routers of that organization are responsible for delivery of the packet to the correct host.
- A type A, or type B network is usually too big to be administered as a single network and is thus divided into subnets. The subnet prefixes are leftmost bits borrowed from the host number.
- Thus all hosts of a subnet have the same subnet prefix.
- The subnet address can be obtained by logically ANDING a subnet prefix with the IP address of any host in the subnet.
- The number of subnetworks in a given network is 2s.
- The number of hosts in a subnetwork is 2h - 2. The -2 is for the subnet braadcast address(All ones) and the subnet address(All zero's)
Network prefix / Length = n	Subnet prefix / Length = s	Host number / Length = h

How do routers do lookups in the case of classful addressing?
- Once a packet is received the router examines the initial bits of the destination address to determine the class of address.
- It then applies the network mask for that class of IP address to obtain the network id.
- It then looks in its routing table to ding out how to route the packet to its destination.

IP address classes (Classful addresses)

Class A
0nnnnnnn	hhhhhhhh	hhhhhhhh	hhhhhhhh

- First bit = 0
- Network bits = 7
  - 2^7 – 2 class A networks
    - 0.0.0.0 – This network
    - 127.x.x.x – Loopback address
- Host bits = 24
  - 2^24 – 2 hosts in each class A
    - Network address – All host bits are zero.
    - Broadcast address – All host bits are one.
- Initial byte = 0-127

Class B
10nnnnnn	nnnnnnnn	hhhhhhhh	hhhhhhhh

- First 2 bit = 10
- Network bits = 14
  - 2^14 class B networks
- Host bits = 16
  - 2^16 – 2 hosts in each class A
    - Network address – All host bits are zero.
    - Broadcast address – All host bits are one.
- Initial byte = 128 - 191

Class C
110nnnnn	nnnnnnnn	nnnnnnnn	hhhhhhhh

- First 3 bits = 110
- Network bits = 21
  - 2^21 class B networks
- Host bits = 8
  - 2^8 – 2 hosts in each class A
    - Network address – All host bits are zero.
    - Broadcast address – All host bits are one.
- Initial byte = 192 – 223

Class D – Multicast address
1110mmmm	mmmmmmm	mmmmmmmm	mmmmmmmm

- First 4 bits = 1110
- Initial byte = 224-247

Class E – Reserved for experimental use
1111rrrr	rrrrrrrr	rrrrrrrr	rrrrrrrr

Initial byte - 248-255