IP(v6)

Features of IPV6 over IPV4
- Expanded addressing capabilities
- No fragmentation
- Fixed 40-byte length header
- No Checksum
- Flow labeling and priority

IPV6 datagram
Version / (4)	Traffic classification / (8)	Flow label / (20)
Payload length / (16)			Next header / (8)	Hop limit / (8)
Source Address(32)
Source Address(32)
Source Address(32)
Source Address(32)
Destination Address(32)
Destination Address(32)
Destination Address(32)
Destination Address(32)

Transitioning from IPV4 to IPV6
- Dual stack approach(Figure 31)
- Tunneling approach(Figure 32)