Link Layer

Services provided by the link layer
- Error detection and correction - Important
- Link access - Important
- Framing
- Reliable delivery
- Flow control

Adapters
- Link layer implementation
- Semi-autonomous unit

Token ring lan Utilization
Maximum length of a frame in a token ring lan is dependent on the propagation delay
The maximum length should be such that the time to transmit the packet should be lesser than the time it takes the first transmitted bit to reach the sender after a trip in the lan.

Utilization of the link = {Time spent transmitting the frame} over {Total Time required}
        = {Number of stations * Time spent by each transmitting the frame} over {Number of stations * Time spent by each transmitting the frame + Ring latency}

Baud
Baud is a unit of transmission specifying the number of symbols or bits per second