Link state routing

- Initially when a router comes up(booted), it learns about its neighbours by sending a special HELLO packet on each point-to-point link.
- It then measures the line cost to each of them by the use of some metric(typically delay or congestion based).
- With this information it builds link state packets. Link state packets are build periodically or when some significant event occurs, such as a line going down or comping back up again or changing its properties appreciably.
- Each node in the network then broadcast link-state packets to all other nodes in the network through the sequence-number-controlled flooding
- A link-state packet of a node contains the identities and costs of the attached links.
- The result is that the network topology and all link costs are identical and is available to the LS algorithm running on each node in the network.
- The LS algorithm itself is the famed Dijkstra's algorithm.

Properties
- It is a global routing algorithms.
- Worst case complexity of O(n^2) if min is found in linear time of O (n)
- Worst-case complexity is O(n log n) if min is found using a heap

Oscillations in link-state routing(Figure 33)
- Oscillations occur in networks using a link-state routing algortihm due to using a dynamic delay congestion based link metric
- They can be avoided by having routers send out link advertisements(ICMP messages) at random times.