Network layer

- Introduction
- Virtual Circuits
- Routers – Forwarding and Routing
- IP(v4)
  - Classless and Classful addressing
  - Source Routing
  - NAT
  - ICMP
  - DHCP
- IP(v6)
- Routing algorithms
  - Link state routing
  - Distance vector routing
- Dealing with scale - Hierarchical routing
  - Routing in the internet
    - Intra-AS
      - RIP
      - OSPF
    - Inter-AS
      - BGP
- Broadcast Routing
- Multicast Routing
Functions of the network layer
- Forwarding
  - A router local action.
  - Process of directing a packet from an input link of a router to one of its own output links.
- Routing
  - A network-wide process.
  - Process of determining a route or a path and sending/receiving packets in a network.

A typical forwarding table
Header Value in Packet	Output link
0000	1
0010	4
1101	5
1000	56
. / . / .	. / . / .

Important network architectures
- Internet
- ATM
- Frame Relay
- X.25

Network service models
Network Architecture	Service Model	Bandwidth Guarantee	No-Loss guarantee	Ordering	Timing	Congestion indication
Internet	Best effort	None	None	Any ordering possible	Not maintained	None
ATM	Constant bit-rate	Guaranteed constant rate	Yes	In-Order	Maintained	Congestion will not occur
ATM	Available bit-rate	Guaranteed minimum rate	None	In-Order	Not maintained	Congestion indication maintained

Jitter
- Also known as packet-delay variation.
- It is the deviation/difference between the end-to-end delay of packets in a flow.
- i.e. you would say that there is jitter if packets are sent from a sender at regular intervals of 't' seconds and at the receiver the packets are not received at exact intervals of 't' seconds. Some packets may arrive at t + %delta t after their previous ones.

Services offered by Virtual Circuits and Datagram networks
At transport layer		At network layer
Virtual Circuit	Datagram network	Virtual Circuit	Datagram network
Offers connection oriented service only	Offers connection oriented(TCP) and connectionless(UDP) service	Offers connection oriented service only	Offers connectionless service only(IP)

Packet switches
- Routers – Switching/forwarding done based on information in a network-layer field.
- Link-layer switches – Switching/forwarding done based on information in a link-layer field.