Random Access protocols

Slotted Aloha(Figure 33)
- Nodes transmit only at the start of slotted intervals
- Nodes capable of detecting collision. When collision occurs the nodes retransmits in subsequent intervals with a probability of p.
- Probability of an arbitrary node successfully transmitting is p(1-p)^{N-1} + p(1-p)^{N-1} + ... N "times" = Np(1-p)^{N-1}
- Mathematics shows that only 37% of bandwidth is utilized
- Collision can occur only at the strt of transmissions

Normal Aloha(Figure 34)
- A decentralized version of slotted aloha.
- Nodes don't wait for the start of a slot to transmit.
- This means that a collision can occur midway through transmission
- Probability of an arbitrary node successfully transmitting is Np(1-p)^{N-1}

Carrier sense multiple access with collision detect – CSMA/CD(Figure 35)
- Nodes sense for any ongoing transmission before beginning their own transmission
- Nodes continue sensing after start of transmission. If another transmission is detected, current transmission is aborted.