Routers - Forwarding and switching

Growth of forwarding tables
Internet routers use the longest-match-prefix-rule(LMPR) to match IPV4 addresses and forward them. This works only if an outgoing link interface is responsible for forwarding all of the contiguous destination addresses.
Of late there are concerns that these blocks of contiguous addresses are not being allocated as large blocks, thus increasing the size of the forwarding tables.

Router architecture(Figure 24)

Decentralized forwarding
- Forwarding is done by the 'network-layer-functionality' chip/module at each input port of a router. This requires lookups into the forwarding table.
- The decentralized forwarding refers to the lookups done by these modules from a copy of the forwarding-table maintained by them locally on-chip/on-module.
- Plain forwarding routers refer to ordinary workstation CPU's being used as routers. They do not have special hardware to do the sophisticated local lookup. In fact the input ports are plain network interface cards. They simply interrupt the processor which does the lookup and forwarding when a packet arrives.

Desirable trait of the input port processing in modern routers
Processing of input packets(lookups) should proceed at line speed, i.e., the lookups must be faster then the rate at which packets are received.

Illustration of performance requirement for lookup
- OC48, a communication link runs at 2.5 Gbps.
- Assume a packet to be of 256 bytes
- Lookup speed needed = {2.5 Gbps} over {256 bytes} = 1220703 approx 1 million/second

Cause of queuing in the input port
Queuing is a result of the input port not being able to forward the packet to the required output port once the lookup is done. This is dies to the switching fabric being used by other input ports at that time.

Switching via memory in traditional computers(Figure 25)
- Interrupt to the CPU(routing processor) from an input port wishing to forward.
- Processor copies packet to its memory via the system bus.
- Processor uses the forwarding table to do a lookup for the required output port
- Processor copies the packet to the buffer of the required output port from memory via the system bus.

Switching via a bus(Figure 26)

Switching via an interconnection network(Figure 27)

Output port and input port of a router(Figure 28)

Cause of queueing in output port
Speed of switching fabric is greater than transmission speed of output link.

Role of packet scheduler at the output port
- A consequence of output port queuing is that a packet scheduler at the output port must choose one packet among those queued for transmission. The selcetion is done
  - On a simple basis using FCFS schedulin
  - Or a more sophiticated scheduling using weitgted fair queueing which shares the outgoing link fairly among the different end-to-end connections.
- Packet scheduling plays a crucial role in providing quality-of-service guarantees.

Head of line blocking(Figure 29)