TCP segment structure

Source port(16)					Destination port(16)
Sequence number(32)
Acknowledgment number(32)
Header length in words(4)	Unused(6)	URG	ACK	PSH	RST	SYN	FIN	Receive window(16)
Checksum of entire segment(16)					Urgent date pointer(16)
Options
Data le MSS

MSS?
Maximum segment size, the maximum application data that can be used to form a TCP segment

MTU?
Maximum transmission unit. The maximum size of the link layer frame that can be sent across a link. It is a property of the link itself.

Maximum size of the TCP header?
24 words = 24 * 4 = 64 bytes

What is the maximum size of a TCP segment?
Maximum size of a TCP header(64 bytes) + Maximum application data encapsulated(MSS)

How is MSS calculated?
- MSS is calculated by a host/sender TCP by first determining the length of the largest link-layer frame that can be sent by the local sending host(the so called maximum transmission unit, MTU)
- Then MSS is set to ensure that a TCP segment(header + MSS) when encapsulated in an IP datagram fits into a single link layer frame(MTU size).

How are sequence numbers used in TCP?
Sequence numbers are used over the stream of bytes in the TCP's send-buffer and not over individual TCP segments.

How does the receiving TCP process detect where the segment ends and hence the end of data as there is no field in the TCP packet signifying the segment or the data length?
It can be calculated by subtracting the combined length of the TCP header and the encapsulating IP header from the total IP datagram length (specified in the IP header).

What is the significance of the urgent mode?
TCP provides what it calls urgent mode, allowing one end to tell the other end that "urgent data" of some form has been placed into the normal stream of data. The other end is notified that this urgent data has been placed into the data stream, and it's up to the receiving end to decide what to do.

Significance of the push flag
It's a notification from the sender to the receiver for the receiver to pass all the data that it has to the receiving process. This data would consist of whatever is in the segment with the PUSH flag, along with any other data the receiving TCP has collected for the receiving process.

Meaning of the acknowledgment number 'X' from A to B
A is expecting a segment with sequence number 'X' from B and that all segments before X have been received.

How is the initial sequence number of a TCP connection selected?
Randomly. This is done to minimize the possibility that a segment that is still present in the network from an earlier, already terminated connection between two hosts is mistaken for a valid segment in a later connection between the two hosts(which also happen to be using the same port numbers as the earlier connection).