Transport Control Protocol - TCP

Why is TCP not a virtual circuit?
- It is built on IP which is a datagram circuit
- The connection state resides entirely on the two end systems.

What are the characteristics of a TCP connection?
- Connection oriented – i.e., establishes connection before it actually communicates
- Fully duplex – communication in both directions simultaneously
- Point-to-point - A TCP connection is between a single sender and a receiver as opposed to between a sender and multiple receivers as in multicasting.

Why is TCP a stream oriented protocol and UDP a message oriented one?
- TCP views data as an unstructured, but ordered, stream of bytes. It's use of sequence numbers reflects this view in that sequence numbers are over the stream of transmitted bytes and not over the series of transmitted segments.
- All data passed on through the socket is stored on in a send buffer and TCP then picks MSS amount of bytes to transmit in a segment. In contrast UDP transmits the exact block of message at a time that the application passes on to it.

TCP segment structure

TCP's data transfer protocol

Flow control

Congestion control

TCP Connection setup and teardown(Figure 50)

What TCP parameters govern the size of the senders window?
Min(CW, RW), where
- RW = Receivers window
- CW = Congestion window

Congestion window and Receive window
TCP parameters which limits the maximum unacknowledged bytes sent by the sender.

Assuming that CW < RW, what is the sending rate of a host into a connection?
CW over RTT , meaning CW bytes are sent per RTT

TCP transmission rate
It is the perceived rate at which TCP transmits data accounting for the wait for ACK. It is not a real transmission rate.

TCP parameters governing the transmission of packets?
- Congestion window _ number of bytes sent cannot exceed CW
- Receivers window – Number of bytes sent cannot exceed RW
- Senders window – Number of bytes sent cannot exceed a maximum of the SW(Management of sequential numbers)

Distinguish between TCP transmission rate and TCP throughput
- Both are mathematically identical quantities expressed in bytes per second.
- Transmission rate refers to the rate at at the senders side
- Throughput refers to the rate at the receivers side. Also throughput is measured in context of the transmission of a fixed quantity, say, a file.

Latency?
In the context of a TCP connection, latency is the time a client waits for after submitting its request to getting the data in tis entirety.

Stall time of a server after the transmission of the k'th window
Time to transmit the first segment(S/R) + Time to get ACK(RTT) – Time to transmit all segments in the k'th windw(2k – 1 S/R)

How can the number of stalls by the server be calculated?
Number of stalls = { (k – 1) * S/R + RTT - 2k – 1 S/R >= 0 }

How many segments will a k'th segment of the TCP slow-start phase have?
1st window → 1 segment
2nd window → 2 segments
3rd window → 4 segments
.
.
.
kth window → 2k-1 segments

What does a TCP connection consist of physically?
- Send and receive buffers
- Variables at both ends
  - Sender side
    - Congestion window
    - Threshold
  - Receiver side
    - Receive window
- Socket connection at both ends