Transport layer

Popular internet protocols and their underlying transport protocols
Application	Application-layer protocol	Underlying Transport protocol
Email	SMTP	TCP
Remote terminal access	Telnet	TCP
Web browsing	HTTP	TCP
File transfer	FTP	TCP
File transfer	TFTP	UDP
Remote file server	NFS	UDP/TCP
Network management	SNMP	UDP
Routing	RIP	UDP
Name translation	DNS	UDP/TCP
Streaming multimedia	Proprietary	UDP
Internet telephony	Proprietary	UDP

End-end principle
Since certain functionality(think error checking) must be implemented on an end-end basis, “functions placed at the lower levels may be redundant or of little value when compared to the cost of providing them at the higher level”.

Difference between bandwidth, throughput and capacity of a channel
- Capacity and bandwidth are the same. Bandwidth is simply the data rate measured in bits per second.
- Throughput is an average rate of successful message delivery over a communication channel. There are factors that affect throughput such as congestion. So while you may buy a certain amount of bandwidth from your provider, your throughput is generally less than the bandwidth.

What are transport later packets called?
Segments

What is the distinction between the logical connection provided by the transport layer and the network layer?
Transport later – Provides logical connection between 2 process in 2 hosts.
Network layer – Provides logical connection between 2 hosts

What type of connections does the TCP and UDP use?
TCP and UDP both use IP which actually is a datagram type of connection.

What are the services implied by a reliable data transfer?
- Guaranteed delivery
- Orderly delivery
- Data integrity

What are the services UDP offers by building-upon/extending IP?
- Process-to-process delivery(Multiplexing and De-Multiplexing)
- Unordered unicast or multicast delivery.
- Error checking

What are the services TCP builds-over/extends from IP?
- Multiplexing and De-Multiplexing
- Error checking
- Reliable inorder unicast data transfer
- Congestion control
- Flow control

What are the services not offered by the transport layer in the TCP/IP suite?
- Real-time delivery
- Bandwidth Guarentees
- Reliable multicast delivery.

What is a socket?
Socket is a software interface between the application and the transport layer used to transfer data between an application process and the transport layer. It is provided by the transport layer

What is demultiplexing?
The process of delivering data in a segment to the correct socket by the transport layer entity at the receiving end of a connection.

What is multiplexing?
Process of gathering the chunks of data pushed by the applications through their respective sockets, encapsulating them into segments and then delivering them to the network layer.

What are port number?
Unique identifier of a socket within a particular host.

How does UDP identify the required socket during demultiplexing?
By examining the destination port number.

How does TCP identify the required socket during demultiplexing?
Since TCP maintains a different connection for each different communication, it identifies the required socket by examining the triple
- Destination port number
- Source port number – To distinguish different users on the same host
- Source IP address – To distinguish hosts

Is a socket a per-process entity?
Not necessarily. A single multi-threaded application process(Web server) may have multiple sockets, one per spawned thread.

Port numbers of popular applications
Applications	Port number
Telnet	23
FTP
HTTP

What is transmission rate of a link?
It is the rate at which a host can push data into the link.

What is utilization of a link?
The fraction of the time a sender is actually busy sending data in a link.
U = L/R over {L/R + RTT}
where L = Length of the packet/segment/datagram, R = transmission rate, RTT = round trip time

Flow control
It is a speed matching service to ensure that the sender sends data at a rate at which the application at the receiving side reads data from the TCP's receive buffer.

Congestion control
Throttling of the transmission rate of the sender due to congestion within network.

What is offered load?
It is the rate at which data is offered to the network by the transport layer. It is less than the rate at which the application offers the same data if the transport layer operates an RDT. This is because the transport layer retransmits lost packets taking up extra time per lost packet

What is throughput of a network connection?
Rate at which the receiver received data