UDP(User Datagram protocol)

Why would applications ever want UDP?
- Finer app control over data transmission due to absence of congestion control.
  - A sender can afford to send data at some minimum sending rate
- Smaller header size
- Simple : No connection states is to be maintained by the end systems.
- No connection establishment.
  - No handshaking
  - Each UDP segment is handled independently of the others
- Applications
  - Streaming multimedia apps which are loss tolerant but rate sensitive
  - DNS and SNMP because these protocols don't involve extended to-and-fro communication. A connection setup would be a waste.

UDP segment structure
Source port(16)	Destination port(16)
Length of segment including header in bytes(16)	Checksum
Application data(lesser than MSS)

How is checksum calculated by the sender UDP?
- The complement of the payload(pseudo IP header + UDP header) is calculated.
  - A sum of all 16 bit words, with 0-padding in the end if necessary is calculated
  - Any overflow is wrapped around.
  - The result is complemented.

How is checksum verified by the receiver UDP?
- The checksum is the complement of the payload((pseudo IP header + UDP header). Adding both should give all 1's
  - A sum of all 16 bit words(pseudo IP header + UDP header), with 0-padding in the end if necessary including the checksum is calculated
  - If no errors are introduced the resultant is all 1's. 1111111111111111

Is the use of the checksum field compulsory in UDP?
- No. Non usage of the checksum field is indicated by having a all zero checksum field.
- If the checksum is calculated and comes up to all zero's, all one's is put in the checksum field. This will not affect the error checking at the receiver side as all zero's is equivalent to all one's in one's complement arithmetic(addition with the carry being wrapped around).