Bus
A bus is a shared communication link, which uses one set of wires to connect multiple sub-systems(Processors, Memory, I/O devices).

Advantage of bus organization
- Cost effective – A single set of wires is shared in multiple ways
- Scalability – Devices can be added
- Interoperability – Peripherals can be moved between computer systems that use the same kind of bus

Disadvantages of bus organization
- Communication bottleneck, possibly limiting the maximum I/O throughput
- Design of bus is challenging

Why is bus design a major challenge?
- Bus must be capable of meeting the demands of the processor as well as the possibly large numbers of I/O devices connected to it.
- Maximum bus speed is largely limited by physical factors: the length of the bus and the number of devices.
- Need to support the range of devices with widely varying latencies and transfer rates

Why are serial buses(using high speed serial point-to-point connection with switches) preferred over parallel buses?
Difficult to run many parallel wires at high speed(required to match the growth in the operating speed of processors, memory and devices) due to clock skew(different wires operating on slightly skewed clock) and reflection(interference in a wire due to its neighbors)

General structure of the bus
- Control lines – Used to signal requests and acknowledgments, and to indicate what type of information is on the data lines
- Data lines – Used to carry information(data, complex commands, addresses) between the source and destination. Some buses use a seperate address bus for addresses.

What does a bus transaction consist of?
A sequence of bus operations that includes a request and may include a response. The request or response may also carry data.
A transaction is initiated by a single request and may take many individual bus operation. It takes as many bus operations required to complete transfer of a memory block to or from memory.
Example: A read request from the processor to a disk might result in the disk putting chunks of data multiple times on the bus and suitably indicating to the processor.

Types of bus transactions
Bus transactions are typically defined by what they do to memory.
- Read transaction(Output) – Read from memory to processor or I/O device
- Write transaction(Input) – Write to memory

Comparison between system buses and I/O buses
Processor-Memory Buses or System Buses	I/O buses
Short	Can be Lengthy
Generally high speed. Matched to the memory system so as to maximize memory-processor bandwidth	Many types of devices connected to them, and often have a wide range in the bandwidth to accommodate all the devices connected to them. They are generally not as fast as the system bus due to the comparative low speeds the IO devices operate at.
	Do not interface directly to memory but use either a processor-memory bus or a backplane bus to connect to memory. ????
There will typically be one system bus in a system to connect the processor with the memory.	There will be many different IO buses in a system. / Examples: / The ISA bus, which is an old low speed bus, soon to be excluded from the PC design. / The PCI bus, which is a new high speed bus. / The USB bus (Universal Serial Bus), which is a new low speed bus. / The AGP bus which solely is used for the graphics card.

Backplane bus
A bus that is designed to allow processors, memory, and I/O devices to coexist on a single bus.

Schemes of communication on buses
- Synchronous
  - The bus includes a clock and all communication of the devices connected to the bus is relative to the clock. The set of steps to be taken is predetermined relative to the clock.
  - Advantages
    - As the protocol is relative to the clock it is simple(does not need to wait for acknowledgments). Can be implemented easily in a small finite state machine.
    - Bus is fast as protocol is predetermined and involves little logic.
  - Disadvantages
    - Every device on the bus must run at the same clock rate. Hence devices with variance in operating frequency cannot be accommodated on a synchronous bus
    - Because they are dependent on the clock so much synchronous buses cannot be too long because of clock skew problems in buses of greater length
  - Example: Processor-Memory bus
- Asynchronous
  - The bus is not clocked. It uses a handshaking protocol.
  - As it is not clocked, it can accommodate a wide variety of devices
  - The bus can be lengthened without worrying about clock skew or synchronization problems.
  - Example: USB buses, Firewire
What is the clock skew problem?
Clock skew is the difference in absolute time between when two state elements see a clock edge. Clock skew arises because the clock signal will often use two different paths, with slightly different delays, to reach two different state elements. Thus two devices on a long bus which are also from a considerable separate different distances from the clock might mis-function on a synchronous bus.

What is a handshaking protocol?
It consists of a series of steps in which the sender and receiver proceed to the next step only when both parties agree thorough the exchange of messages or signals.

Split transaction protocol
- It is asynchronous transaction protocol where the bus is released in the middle of a bus transaction when it is not being used to transmit information
- Increases the effective bus bandwidth if the memory is capable of handing overlapping requests
- Used by multiprocessors sharing a memory.

Comparisons between serial and parallel buses
Serial bus	Parallel bus
A single distinct link or wire is used to transmit the data stream	A number of distinct wires or links are used at the physical layer for the transmission of a data stream
	Speed
	Cable length
	complexity
space
crosstalk