Control hazards
Control hazard
An occurrence in which the proper instruction cannot begin in the expected proper cycle because the instruction that was fetched is not the one that is needed; that is, the flow of instruction addresses is not what the pipeline expected. This happens due to conditional branches.

How can the effects of control hazards be prevented/lessened?
By using some sort of prediction strategy. Then, either the next sequential instruction(branch-not-taken) or the instruction at the branch address can be pushed into the pipeline.

Does this mean that no stall is required if a predictor is used?
No. There is a penalty(for the case the predictor says that we must branch now) as the branch condition which decides the flow of execution is calculated only in the 3rd stage(ALU). The IF and ID will now have to be idle(i.e., a stall time of 2 cycles) until the branch address is calculated.
Clock cycle	1	2	3	4	5	6
Instructions
I1(beq $s1, $s2, 25)	IF	ID	EX	MEM	WB
stall
stall
Predicted instruction				IF	ID	EX

Branch condition is calculated only here

Solution for the above : Reduced branch delay
- Reducing the delay in branches means that the branch-condition calculation is moved to an earlier stage(instead of in the ALU stage) so that the branch penalty is now just one cycle.
- This also reduces the amount of work which should be discarded by the pipeline in case of a prediction does wrong.
- Also since most of the branch testing rely only only simple tests and that these tests can be done with a small number of gates and not a full fledged ALU, the reduced-branch-delay becomes a solution even without prediction.

Static prediction
- Predict always taken
  - Continue with the sequential execution assuming that the branch will always be taken, flushing the pipeline when the prediction is wrong.
  - This approach works ok for a pipeline with a smaller number of stages. But for a pipeline with a large number of stages, the branch penalty increases when measured in terms of clock cycles. A greater amount of instructions and the work done on the has to be flushed
- Predict always untaken
  - Same as above except that the branch is always not taken

Dynamic prediction
- Prediction of branches at runtime using runtime information
- Make use of a branch prediction buffer or a branch history table. It is a small memory that is indexed by the lower portion of the address of the branch instruction and contains one or more bits indicating whether the branch was recently taken or not. It has one entry per branch taken.
- 1-bit prediction scheme
  - Each entry in the branch prediction buffer has one bit which records if this branch was previously taken or not. The branch prediction is done according to this information.
  - Every time the prediction is proved wrong the bit is flipped
  - Has a performance shortcoming when dealing with loops. It will likely predict incorrectly twice, instead of one(i.e. The expected one at the end). This unexpected incorrect prediction is at the start of the same loop the next time. Since in the previous iteration the last branch was taken, the bit will be set to indicate that. This results in the first branch of the loop this time being wrong.
- 2-bit prediction scheme
  - Each entry in the branch prediction buffer has two bits which records if the previously this branch was taken or not. The branch prediction is done according to this information.
  - The prediction is changed only when it is wrong twice
  - Works well with loops
- If the branch prediction buffer is designed to hold the branch address associated with the branch instruction as well, there will be no delay associated with the calculation of branch condition when used with the reduced-branch-delay design. Such prediction buffers are called branch target buffers

Correlating predictor
A branch predictor that combines local behavior of a particular branch and the global information about the behavior of some recent number of executed branches.

What is the logic behind a correlating predictor?
Researchers have noticed that using information about both a local branch and the global behaviour or recently executed other branches together yields greater prediction accuracy.

Tournament branch predictor
A branch predictor with multiple predictions for each branch(one based on the local history of that branch and the other based on the global history of other recently executed branches) and a selection mechanism that chooses which predictor to enable for each branch.

Delayed branches
- This is another mechanism of avoiding the penalty or stall cycles associated with branching.
- Here the compiler fills the slot next to the branch instruction(the branch delay slot) with an instruction that is not affected by the branch and that does not affect the branch. Moving this instruction to the branch delay slot should obviously not affect the correctness of the program.
- No prediction or the extra hardware associated with the reducing-branch delay is needed in this case.
- The instruction/s in the branch delay slot occupies the pipeline while the branch instruction is completely executed to determine whether a branch should be taken or not.