Data hazard
- An occurrence in which a planned instruction cannot start in the proper clock cycle because data needed to execute the instruction is not yet available.
- Generally speaking, the stage which fetches the operand cannot do so in the specified lock-step cycle as the operand it needs to fetch will be written into the register file in later clock cycles by previous instructions.
Example : Consider,
            add $s0, $t0, $t1
            sub $t2, $s0, $t3

$s0 is available only after the 5th clock cycle

Clock cycle	1	2	3	4	5	6
Instructions
I1(add $s0, $t0, $t1)	IF	ID	EX	MEM	WB
I2(sub $t2, $s0, $t3)		IF	ID	EX

Want $s0 here. A data hazard

Solution to data hazard
Forwarding or bypassing – A method of resolving a data hazard by retrieving the missing data element from the internal buffers rather than waiting for it to arrive from a programmer-visible registers or memory.

Clock cycle	1	2	3	4	5	6
Instructions
I1(add $s0, $t0, $t1)	IF	ID	EX	MEM	WB
I2(sub $t2, $s0, $t3)		IF	ID	EX	MEM	WB

Value of $s0 is forwarded from EX of I1 to EX of I2. The ID of I2 only fetches $t3

Load use hazard - Instances where forwarding cannot prevent a stall
A data hazard in which data requested is not yet available as the previous load instruction makes it available only in the end. A load use hazard occurs when an R-format instruction following a load tries to use the data
lw $s0, 4($t0)
sub $t2, $s0, $t3

Here $s0 is available only after the 5th clock cycle. A value from the 5th clock cycle can't be forwarded to the 4th clock cycle

Clock cycle	1	2	3	4	5	6
Instructions
I1(lw $s0, 4($t0))	IF	ID	EX	MEM	WB
I2(add $s0, $t0, $t1)		IF	ID

How can a load-use hazard be resolved
By resorting to a pipeline stall or a bubble. It is a stall initiated in order to resolve a hazard.