Expanding opcode technique
- Provides a compromise between the need to have a rich set of opcodes and the need to have short instruction lengths
- Example
  Consider a 3 address machine with 4 bit opcodes and 4 bit registers. Normally we could have 24 3 address instructions. In the expanding opcode technique we could have
  - 24 – 1 = 15, 3-address instructions
    0000 R1 R2 R3
    …
    1110 R1 R2 R3
  - 24 – 1 = 15 2-address instructions
    1111 0000 R1 R2
    …
    1111 1110 R1 R2
  - 24 – 1 = 15 1-address instructions
    1111 1111 0000 R1
    …
    1111 1111 1110 R2
  - 24 = 16 0 address instructions
    1111 1111 1111 0000
    …
    1111 1111 1111 1111
    for a total of 61 instructions
    Note that this is not the only way to expand the opcode.
- One downside to using this technique is that decoding is more complicated. It is no longer looking at some n fixed bits in the instruction and accessing the operands. Now, a determination of which type of instruction must be done before proceeding further.