Faster addition : Carry Lookahead

Assumptions
The delay across AND and OR gates is T seconds

n-bit ripple carry adder
- s_i = a_i %UxE137 b_i %UxE137 c_i where ai, bi are the i'th single bit operands and ci is the i'th carry-in bit
- c_{i+1} = a_i b_i + b_i c_i + c_i a_i where ci+1 is the carryout of the i'th bit
- Delay = Time to calculate the 0'th sum and carry bits +
    + Time to calculate the 1st sum and carry bits +
    + … + Time to calculate the n-1'st sum and carry bits
    2T + 2T + … n times
    = 2Tn

n-bit carry lookahead adder
- s_i = p_i %UxE137 c_i and c_{i+1} = p_i c_i + g_i where
  - p_i = a_i %UxE137 b_i is the carry propagate as it is the variable linking the i'th carry to the i+1'th carry
  - g_i = a_i b_i is the carry generate as it can generate the carry-out even when the carry-in is 0
- Delay = Time to calculate all carry propagate and generate bits in parallel
    + time to calculate all sum and carry bits in parallel
    = 2T + 2T
    = 4T
  - It is practically not feasible to implement the plain single level carry lookahead when n is large(greater than 4 say) as the number of input gates needed to calculate the carry bits become large and it is not feasible to manufacture gates with large inputs.

n-bit ripple carry adder using m-bit CLA adders(m = kn and m is small, say bold {m le 4} preferebly)
- The k m-bit CLA's are connected in serial with the carry-out of one connecting to the carry-in of the other
- Delay = Delay in 1st m-bit CLA
    + Delay in the 2nd m-bit CLA
    + … + Delay in the k'th m-bit CLA
    = 4T + 4T + … k times
    = 4Tk

n-bit , x-level CLA adder
- Delay = Time to calculate the first level carry propagate and generate bits in parallel
    + Time to calculate the 2nd level carry propagate and generate bits in parallel
    + … + Time to calculate the x'th level carry propagate and generate bits in parallel
    + Time to calculate all the sum and generate bits in parallel
    = 2T + 2T + … x times + 2T
    = 2T(x+1)

Designing a multi-level CLA adder
- The first level of carry propagate and generate bits are calculated as before
- The sum bits can be immediately calculated now
  s_i = p_i %UxE137 c_i
- The carry-out bit is calculated as follows
  - The propagates and the generate bits are grouped such that the next level of 'super' propagates and generates can be calculated using gates in circuits with less number of inputs(<= 4)
  - The 'super' propagate signal is true only if each of the bits in the group propagate the carry. Example : P0-3 = p0p1p2p3
  - The 'super' generate signal is true only if the carryout of some bit is carried to the most significant bit of the group. Example G0-3 = g3 +g2p3 + g1p2p3 + g0p1p2p3
  - The nesting continues until the carry-out can be calculated using a circuit with gates having a small(<=4) amount of inputs.