IEEE 754 representation

The non regularity in representation of successive floating point numbers
The difference between two successive floating point numbers do not vary regularly. This is because there are a finite amount of bits to represent the fractional part of floating point numbers. As the numbers become larger, the finite mantissa approximates the large number by assuming zeroes to the least significant places.
Example: The largest and 2nd largest number representable in a single precision floating point representation and the difference between them are as below
0	11111110	11111111111111111111111

alignl 1.11111111111111111111111 times 2^{254 - 127} = 1.11111111111111111111111 times 2^127 newline ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~"=" 111111111111111111111111 times 2^104 newline ~~~~~~~~~~~~~~~~~~"=" (2^25 - 1) times 2^104

0	11111110	11111111111111111111110

alignl 1.11111111111111111111110 times 2^{254 - 127} = 1.11111111111111111111110 times 2^127 newline alignl ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~"=" 11111111111111111111111 times 2^105 newline alignl ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~"=" (2^24 - 1) times 2^105 = 2^25 - 2 times 2^104

The difference between them is 2^104
- The difference between any two successive numbers which can be represented with the same exponent, e, is constant.
- There is a jump in the difference between successive numbers whose exponent greater than e.
- The largest difference between two successive representations of floating point numbers is 2^{2^e - m}