Instruction set architecture

Instruction set
The vocabulary of commands understood by a given architecture

Instruction set architecture or architecture
- An abstract interface between the hardware and the lowest level software of a machine that encompasses all the information necessary to write a machine language program that will run correctly.
- This interface includes specifications regarding
  - Registers
  - Memory access
  - IO and so on

Implementation
A hardware that obeys a particular architecture abstraction

Word
The natural unit of access in a computer.

Classification of instruction set architectures based on the internal storage available to the processor(Figure)
- Stack architecture
  - Has a stack based organization.
  - Instructions which perform computation implicitly act on the top two operands on the stack and store the result back in the stack.
  - Only the 'push' and 'pop' instructions access operands through addresses.
- Accumulator architecture
  - For this to work, a second address is implicit, a processor register called the accumulator(AC). The accumulator contains one of the operands and is implicitly used to store the result of every operation.
  - Most of the early architectures were stack or accumulator architecture
- General-purpose register architecture
  - Register-memory architecture
    - Memory can be accessed as a part of any instruction.
  - Register-register or Load-store architecture
    - Memory can be accessed only as a part of load and store instructions.
    - Most of the new architecture designed after 1980's are load-store register architectures.
      - Registers as a medium of storage are faster than memory.
      - Registers are more efficient for the compiler to use than other forms of internal processor storage(stack, accumulator).
  - Extended accumulator or special purpose register architecture
    - There are restrictions on the uses of registers other than the accumulator.

Classification of instruction set architectures based on the number of addresses in the instruction
- Zero address architecture(Stack architecture)
- One address architecture(Accumulator architecture)
- Two address architecture
  - Register-memory architecture
  - Memory-memory architecture
    - All operands are kept in memory.
    - This type of architecture is not shipped today
- Three address architecture
  - Register-register architecture
  - Memory-memory architecture

Programs in typical architectures to compute Y = (A – B) / (C + (D * E))
Stack machine / (0, 0)	Accumulator / (1, 1)	Register Memory / (1, 2)	Register-register / (0, 3)
PUSH E / PUSH D / MUL / PUSH C / ADD / PUSH B / PUSH A / SUB / DIV / POPY	LOAD D / MUL E / ADD C / STORE Y / LOAD B / SUB A / DIV Y / STOR Y	LOAD R1, D / MUL R1, E / ADD R1, C / LOAD R2, A / ADD R2, B / DIV R1, R2 / STORE R1 , Y	LOAD R1, D / LOAD R2, E / MUL R1, R1, R2 / LOAD R2, C / ADD R1, R1, R2 / LOAD R2, A / LOAD R3, B / SUB R2, R2, R3 / DIV R1, R1, R2 / STORE R1 , Y

The notation (m, n) means a maximum of m memory operands allowed out of n total operands

Advantages and disadvantages of the three most common types of general-purpose register computers
Type	Advantages	Disadvantages
Register-register / (0, 3)	Simple, fixed-length encoding. / Simple code generation model. / Instructions take similar number of clock cycles to execute.	Higher instruction count than architectures with memory references in instructions. This leads to larger programs
Register-memory / (1, 2)	Data can be accessed without a separate load instruction leading to relatively lower instruction count and hence smaller programs	The need to encoding a relatively bigger memory address in each instruction may restrict the number of registers allowable in the architecture / Clocks per
Memory-memory / (2, 2) or (3, 3)	Most compact.	Memory accesses create bottleneck.