Microcoded control unit(Figure 31)

Principle
- The hardwired approach to control unit design treats the relationship between control inputs(the opcode) and control outputs as a series of boolean functions, one for each of the control signals.
- In the microcode approach, the relationship between inputs and outputs is treated as a memory system. Control signals are stored as words in a microcode memory. At each clock tick during a particular instruction execution, the appropriate control word is fetched from microprogram memory to supply the control signals.

Microcode memory
- The execution of one normal instruction in a pipelined instruction takes multiple cycles and control signals are needed to be asserted in each clock cycle to guide the execution.
- In a microcoded implementation, this means asserting a sequence of control words, one for each stage of the instruction execution in the pipelined processor implementation.
- The microcode memory thus consists of all possible control words needed to form sequences of words corresponding to the execution of any instruction in the instruction set.
- Also, in a typical large instruction set, it is likely that there are opportunities to reuse control-word sequences in interpreting similar instructions or in implementing operand access and decoding. Structuring the microcode memory in terms of subroutines enables sharing of each microprogram sequences without having to duplicate microinstructions. For example, in the MIPS architecture,
  - All instructions(R, I and J type) share the same control signals for their instruction fetch phase, that which parallely increments the PC and fetches the instruction.
  - Register versions of arithmetic(add, addu, sub, subu), logical operations(and, andu, or, nor) and register versions of conditional operations(slt, sltu) operations share the same signals for their ALU phase, that which performs the specified operation on the two source registers.
  - Memory access instructions(lw, lbu, lhu, sw, sb, sh) and the immediate versions of the arithmetic instructions(addi, addiu) share the same control signals for their ALU stage, that which adds one source register with the sign-extended immediate field.
  - Conditional branches(beq, bne) share the same signals for their ALU phase, that which enables subtraction on the source registers to test the equality.

Symbolic format of a control word
Name of subroutine if this word represents the start of one	Control signals	Sequencing control

Sequencer
- Since generating control signals for an instruction execution involves asserting multiple control words, there is a need for some kind of sequencing to access and assert the exact sequence of control words from the control store which will guide the current instruction through the datapath.
- The sequencer is a small combinatorial circuit which loads the address of the next control word into the microprogram counter, so that the control word can be accessed and asserted.
- It loads this address based on the sequencing control information present in the currently asserted control word. This information specifies one of the following.
  - Start asserting control signals to start the execution of a normal instruction, i.e., the ones required to fetch the instruction in the first stage of a pipeline.
    - The sequencer locates the address of this control word by doing a lookup in the dispatch table of the sequencing control information and loads it into the microprogram counter.
  - Assert control signals present in the next sequential address of the microcoded memory
    - The sequencer adds one to the current address and loads it into the microprogram counter.
    - This sequencing control information is specified when continuation of assertion of control words of a subroutine is required.
  - Load the control word by doing a lookup in the dispatch table on the name specified.
    - The sequencer locates the address of control word by doing a lookup in the dispatch table of the sequencing control information and loads it into the microprogram counter.

Horizontal and vertical microprogramming
- In horizontal microprogramming, the control signals in the control word are in a 1-1 correspondence with the control signals needed.
- In vertical microprogramming, mutually exclusive signals are grouped together and are represented in the encoded form in the control word. Thus the length of the control word is less relatively at the cost of decoding the signals before asserting them. Thus m groups of mutually exclusive signals with each group containing n_1, n_2, …, n_m signals, can be represented in 2^{n_1}+ 2^{n_1} + ... + 2^{n_m} bits in the control word.

References
- Heuring
- Patterson