Pipelining

Pipelining is an implementation technique whereby multiple instructions are overlapped in execution; It takes advantage of parallelism that exists among actions needed to complete a instruction.

What is the primary requirement in designing a pipeline?
Independent, separate resources for each stage. Existence of parallelism among instructions(Instruction level parallelism).

How does pipelining improve performance?
By increasing throughput as opposed to decreasing the execution time of an individual instruction.

Stage of a pipeline
The independent hardware unit of the processor which does a unit of task, aiding in the execution of an instruction.

Throughput of a pipeline
Is the amount of instructions that exit the pipeline per unit time.

Why is the length of a processor cycle determined by the slowest pipe stage?
Because the stages of the pipeline are hooked together, the stages must be ready to move at the same time. Because all stages proceed at the same time, the length of a processor cycle is determined by the time required for the slowest pipe stage.

Five stages of a MIPS pipeline
1. Instruction fetch(IF) - Fetch instruction from memory and place it in the instruction register.
2. Instruction decode(ID) - Read registers while decoding the instruction and place them in the source registers of the ALU.
1. Execute or address(EX) – Do an ALU operation in aid of a computation or to calculate an address and place them in an intermediate register
2. Access an operand from memory(MEM)
  1. If the access is a read from memory(which occurs during the ld instruction), place the operand in an intermediate register.
  2. If the access is a write to memory(which occurs during the sw instruction), write the operand from the designated register to memory.
3. Write the result into the register(WB) – Only during load

Intermediate registers
Are programmer invisible registers placed between the pipelining stages to store the result of the particular stages after the completion of each cycle. At the start of the next cycle, a stage makes used of the value in the intermediate register containing the result of the previous pipeline stage.

A graphical representation of a sample pipeline with 5 stages

Stage ID is processing I1 in the 2nd clock pulse

Wind-Down
Start-up
Fully occupied

Clock cycle	1	2	3	4	5	6	7	8	9	10	11	12	13
Instructions
I1	IF	ID	EX	MEM	WB
I2		IF	ID	EX	MEM	WB
I3			IF	ID	EX	MEM	WB
I4				IF	ID	EX	MEM	WB
I5					IF	ID	EX	MEM	WB
I6						IF	ID	EX	MEM	WB
I7							IF	ID	EX	MEM	WB
I8								IF	ID	EX	MEM	WB
I9									IF	ID	EX	MEM	WB

Stage ID is idle. It cannot work on I2 because I2 is not yet processed by A. Stage B depends on the processing done by A

What are the reasons for a practical pipeline to not be as fast as the theoretical model?
- If the number of instructions are not relatively large compared to the number of stages in a pipeline.
  - In any pipeline, not all stages of the pipeline are in use in the start-up and wind-down phases. In this situation, the inefficiency of these two phases are comparable to the efficiency of the phase where all stages are being made use of if the number of instructions is small.
  - When the number of instructions is very large, the effect of this inefficiency is negligible
- Pipeline is unbalanced.
  A pipeline is unbalanced if all of its stages do not have the same latency. A faster stage, say the ID stage, after decoding instruction In, cannot proceed to decoding In+1 as the longer EX stage will not have finished with In-1 and thus will require for the ID stage to wait(During which ID will be idle) for it(EX) to read its(ID) buffers. Thus all stages will essentially have to proceed in lockstep w.r.t. one another.
- Pipelining overhead
  There is some overhead involved in moving data from buffer to buffer and in performing various preparation and delivery functions. This overhead can appreciably lengthen the total execution time of a single instruction. This is significant when sequential instructions are logically dependent, either through heavy use of branching or through memory access dependencies(data hazards)
- Conditional branches
  A condition branch by the virtue of the possibility of forcing the execution of a non-sequential instruction can invalidate several fetches or more generally, invalidate the work done on the instructions next to the current one.
- Pipelining hazards
  Situations in pipelining when the next instruction cannot complete in the next cycle
  - Structural Hazard
  - Data hazard
  - Branch/Control hazard

How does the architecture of MIPS lend itself to pipelining
- All instructions are of the same length – This restriction makes it easier to fetch instructions in the first stage and to decode them in the second. Variable length instructions(like in the IA-32) means that fetching takes variable times
- Few instruction formats, with the source register fields being located in the same place in each instruction – This symmetry means that the second stage can begin reading the register file at the same time that the control is decoding the opcode.
- Memory operands only appear in loads or stores in MIPS – This restriction means that the execute stage can be used to calculate the address and the memory can be accessed in the fourth stage
- Each instruction writes at most one result and does so under the end of the pipeline – This lends itself to forwarding, aiding in the resolution of data hazards. Forwarding is hrder if there are multiple results to forward per instruction or they need to write a result early on in instruction execution

What factors from a pipelining perspective determine the length of the CPU clock cycle?
- Intuitively, to ensure that all pipeline stages operate in a lockstep, the length of the CPU clock cycle is usually equal to the time required by the longest pipeline stage. In this case all stages take one clock cycle.
- The pipeline can also be designed such a clock cycle more closely matches the shortest stage but is integrally divisible into the other stages. This ensures that the pipelining latency is reduced.

Time between instructionspipelined = {Time between instructions of a nonpipelined design} over {Number of stages}