Structural hazard
- The hardware cannot support a combination of instructions simultaneously in the pipeline.
  - Example1 : Assume that the MIPS architecture does not have a separate memory for data and instructions. Then in the same cycle that the 4th instruction is trying to fetch itself from memory, the first instruction would be trying to access data for a read or a write. Both cannot be done simultaneously
Clock cycle	1	2	3	4	5	6	7	8
Instructions
I1	IF	ID	EX	MEM	WB
I2		IF	ID	EX	MEM	WB
I3			IF	ID	EX	MEM	WB
I4				IF

Accessing memory in the same cycle.

  - Example 2 : A machine has only one register-file write port, but the pipeline wants to perform two writes in a clock cycle