Validation based protocols

When are validation based protocols used?
Consider the situation where a majority of the transactions are read-only transactions. As the number of conflicts is very low in these cases, a typical concurrency-control scheme would impose a significant overhead of code execution(concurrency control code) and possible delay in transactions. A validation scheme imposes less overhead for these situations only.

The scheme
- Every transaction, Ti is divided into three distinct phases
  - Read phase – Does all the required reads. Does all the calculation and stores the corresponding results in temporary variables
  - Validation phase – Checks if the transaction can safely write to the database without causing a violation of serializability. The validation test for a transaction Ti+1 is successful if either of the two conditions are true. For all transactions Ti with Validation(Ti) < Validation(Ti+1),
    - Finish(Ti) < Start(Ti+1). This maintains serializability in a trivial manner, i.e., by creating serial schedules
    - Ti does not write on any data elements which are being read by Ti+1 and Ti finishes execution before Ti+1 starts validation,i.e., Finish(Ti) < Validation(Ti+1). The later condition ensure that the writes of the two transactions do not overlap and the former ensures that writes of Ti does not effect Ti+1
  - Write phase – If the validation phase was successful, the writes occur to the database. Else the system rolls back the transaction.
- Cascadelessness and hence recoverability is ensured as Ti+1 operates on data written by Ti only after Ti commits