Combinational Circuits - Morris Mano
Combinational circuit
- Half adder
- Full adder
- Full adder in terms of two half adders
- Concept of Boolean subtraction
- Half subtracter
- Full subtracter
- Codes – BCD, Excess – 3, 84-2-1, 2421, Reflection code
- Logic Function to Boolean function
- Conversion to multilevel NAND and NOR circuits
- NAND/NOR circuits to Boolean function
- Exclusive-or and equivalence function
  - Have 2^n/2 min-terms for a Boolean function of n variables
  - XOR gates are used to implement adders and subtracter's as the respective functions have 2^n/2 min-terms with each min-term having odd number of 1's
  - Complement of XOR function is used to implement a odd parity bit generator as it has min-terms with even number of 1's. Complement of XOR is not XNOR in this case as the parity function is composed of 3 variables and in case of 3 variable functions XOR and XNOR are equivalent
  - Parity bit checker is implemented using xnor as the min-terms of the function have even number of 1's

Combinational Logic using MSI and LSI – Morris Mano
- Design using MSI and LSI
- Binary parallel adder IC
  - BCD to excess-3 converter using above IC
- Single digit BCD adder
- 4-bit magnitude comparator
- Decoders
  - Effect of indiscriminate simplification of don't-care conditions
  - Implementation of decoders using NAND gates – Min-terms in complemented form
  - Construction of 4*16 decoders with 3*8 decoders
  - Construction of 4*16 decoders with 1*2 decoders without using a not gate
- Encoders
  - Octal to binary encoders
- Multiplexers
  - Decoders as multiplexers, selection lines, Input lines
  - Quadruple 2-1 line multiplexers
  - Combinational logic implementation using ROMS

What is the concept behind the solving boolean functions using multiplexers?
A boolean function expressed in a sum of min-terms format essentially says that the function is true whenever atleast one of its constituent functions is true.

By sticking the selection lines with any three input variables and by configuring the 2^n input lines with the 4rth input variable such that the output is true only when a combination of any one input line and the n selection lines resemble any one of the min-terms of the function we can simulate a given boolean function

Usefulness of enable inputs in IC's
Enable lines are convenient features for connection two or more IC packages for the purpose of expanding digital function into a similar function with more inputs and outputs
Example: A 4*16 decoder can be formed using 15 1*2 decoders(1 in the first level, 2 in the 2nd level, 4 in the 3rd level and 8 in the 4th level)

Transferred from hard copy
Decoder(n to 2^n ) - Figure 36
Combinational circuit that converts binary information from 'n' input lines to a maximum of 2^n unique output lines. In effect it gives signals representing all the possible min-terms of those 'n' input lines.

Number of maps needed to solve several output functions which are all mutually exclusive to each other
One. Since the outputs for all functions are mutually exclusive to each other.

Implementation of Boolean functions using decoders
For a given number of input lines, the decoder is capable of generating all the possible min-terms. Express the Boolean function as a sum of min-terms. Use OR gates in conjunction with decoders to implement it.

Encoders( bold 2^n to n) – Figure 37
Combinational circuits which encode any of the of the 2^n input lines into an n-bit code.

Priority encoders( bold 2^n to n) – Figure 38
- Encode the highest priority line of the possible 2^n input lines into an n-bit code.
- Used to design interrupt circuits

Multiplexer( bold 2^n to 1) – Figure 39
- Combinational circuit which selects binary information from one of the 2^n input lines and directs it to a single output line. This direction is carried out with the help of n selection lines.
- Used for connecting 2 or more sources to a single destination
- Used for constructing a common bus system.

Multiplexer using a decoder
- Add 2^n input lines to the 2^n AND gates of a n to 2^n decoder
- OR the output of the 2^n AND gates.

Combinational logic implementation using multiplexers
- A n + 1 variable combination function can be implemented by a 2^n to 1 multiplexers
- The n selection lines of the multiplexer are given the inputs in the following order
  - The lest frequently varying selection line according to the multiplexer's selection line is given the corresponding least frequently varying input according to the truth table
  - The second lest frequently varying section line is given the second least frequently varying input
  - And so on …
- The signals to the input lines are determined by seeing how the corresponding min-terms behave when given the remaining input.

Cost of implementing combination logic using decoders and multiplexers
- Decoders – One OR gate for each function, but generate all min-terms. Therefor suitable for a circuit with a large number of functions
- Multiplexer – One multiplexer for each function. Suitable for a circuit with small number of functions

ROM(Read only memory) – Figure 40
- A combination circuit which has OR gates connected to the outputs of the decoders(min-terms)
- ROM is specified by the number of AND gates of the decoder(min-terms) and the OR gates.
  2^n times m
- Once programmed, the ROM can be seen as giving out an m-bit word(the output of the OR gates) for all possible 2^n addresses of input( 2^n addresses can be specified with the n input lines)
- Thus the specification of ROM can be seen as giving an m-bit word for all the 2^n addresses possible.
- Number of programmable links = Links connecting the output of the 2^n AND gates of the decoders and each of the m OR gates = 2^n * m
- ROM's can be wasteful
  - Logic functions can have don't care conditions which are necessarily decoded
  - Logic functions may have min-term which are independent of a particular input. Such min-terms are formed by decoding complete min-terms and OR'ing them
    Example AB = ABC + ABC'

Mask Programming
ROM programming done by manufacturer according to a specified truth table.

PROM(Programmable ROM)
ROM programming done using PROM programmers. Electrical signals are applied from the output to break links of the OR gate inputs.

EPROM and EAROMS
ROM's which can be erased using ultraviolet light(EPROM) and electrical signals(EAROMS)

PLA – Figure 41
- Programmable logic array. Construction is similar to ROM. However inputs are not completely decoded. Not all mintersm are generated. This is achieved by the AND gates of the decoder also being programmable apart from the OR gates
- Number of programmable links = Links connecting the n input to the k AND gates + Links connecting the n complementing inputs to the l AND gates + Links connecting the k output os the AND gates to each of the m OR gates + m links for bypassing the complement output = nk + nl + km + m