Sequential circuits

Sequential circuit
A circuit whose current state is dependent on the state of memory elements apart from inputs

Synchronous sequential circuit
Sequential circuits whose state change at fixed discrete intervals of time

Asynchronous sequential circuits
Sequential circuits whose states change at any instant of time, based on when inputs are applied

Clocked sequential circuits
Synchronous sequential circuits that use clock pulses to regulate state change

Flip-flops
Sequential circuits which hold a bit of binary information indefinitely(as long as power is supplied) until prompted by an input signal to switch states.

How to determine the function of a latch or a flip-flop from the logic diagram?
Two gates, both being NOR or NAND are used. Since the output of one gate is used as the input to the other gate and vice-verse choose an input to one of the gates such that the output is not dependent on the other input at all,
i.e.,
- Choose S&R/J&K to be 00 if NAND gates are used
- Choose J&R/J&K to be 11 if NOR gates are used
Tracing the behavior is then mechanical.

Characteristic table of a flop-flop(Figure 35)
Defines the logical property of the flip-flop and completely characterizes its operation in the sense of defining its next state for all possible input values.

Excitation tables of flip-flops?(Figure 35)
Lists the required inputs for a given change of state.

State table
Is a tabulation listing the transactions of flip-slop states and the output in accordance to the given inputs.

State diagram
A diagrammatic representation of the state table

State equation
An algebraic expression which specifies the condition for slip-slop transition

State reduction
Reducing the number of states in a sequential circuit without affecting the input-output relationship

State the algorithm of state reduction
Tow states are said to be equivalent, if for a set of inputs they give the same outputs and transition to the same state of an equivalent state.