Cut-Sets

Cut-set
In a connected graph, a cut-set if a minimal set of edges whose removal from G leaves G disconnected.

What happens to the rank of a graph with the removal of a cut-set?
The rank of the graph gives the number of branches of a spanning tree of the graph. A cut-set by the virtue of it disconnecting property contains exactly one branch of a spanning tree. Thus the rank of the graph reduces by one with the removal of a cut set.

Applications of cut-sets
- Used to identify weak spots in a communication net.
- For this purpose all cut-sets of the corresponding graph are listed out and the ones having the smallest number are identified.
- Thus the main requirement is a method to systematically list out all cut-sets of a graph
- All cut-sets of a graph can be generated by following the below method
  - List out all the fundamental cut-sets w.r.t to any given spanning tree of the graph
  - Generate all cut-sets by repeatedly applying the ring-sum(Exclusive-OR), %UxE137 , operation on the available cut-sets.

Properties
- Every cut-set of a graph contains at least a branch of every spanning tree of G.
- A minimal set of edges containing at least one branch of every spanning tree is a cut-set.
- Any circuit of the graph has an even number of vertices common with any cut-set of the graph.
- The minimum number of non-cutset-vertices of a tree is 2. Think of a tree with only one child per node except for the leaf.

Fundamental cut-set
A cut-set containing exactly one branch of a spanning tree T is called a fundamental cut-set w.r.t. T

Relationship between 2 cut-sets of a graph
The non-common edges of any two cut-sets of G is
- A cut-set or
- Edge disjoint union of cut-sets

Relationship between chords forming fundamental circuit and branches of a spanning tree of a graph G
- w.r.t a spanning tree, T, a chord c_i that determines a fundamental circuit is a part of every fundamental cut-set associated with the branches of the fundamental circuit and no other.
- w.r.t a spanning tree, T, a branch b_i that determines a fundamental cut-set is a part of every fundamental circuit associated with the chords of the fundamental cut-set and no other.

Edge connectivity
- Minimum number of edges whose removal leaves a graph disconnected.
- Rank of graph reduces by 1.
- Is the number of edges in the smallest cut-set.
- Edge connectivity of a tree - 1

Vertex connectivity
Number of vertices to remove to disconnect the graph
Vertex connectivity of a complete graph – Meaningless

Bridges
Single edges which separate a graph are called bridges

Articulation points
Single points which separate a graph are called articulation points

Separable graphs
- Graphs with vertex connectivity of one.
- In a non-separable/bi-connected graph the edges incident on each vertex forms a cut-set as a removal of those edges disconnects the graph forming two components with one formed using only the one vertex.
- In a separable graph, removal of the edges incident on the cut-vertex forms two component graphs, neither of which contain the cut-vertex. Thus they do not form a cut-set.
- Application - Determining the best way of connecting nodes in a network with a given number of links such that the network is as invulnerable to destruction as possible.

Vertex with the smallest degree of a graph
Mathematical average of degree of a vertex = 2e over n
Therefore vertex with smallest degree = vertex connectivity le left lfloor {2e} over n right rfloor

vertex connectivity le edge connectivity ???

Vertex disjoint paths
Paths which have no vertices except the terminal vertices in common.

Edge disjoint paths
Two paths in a graph that do not have any edges in common.

k-connected graph
Vertex connectivity is k, i.e., every pair of vertices are connected by atleast k vertex disjoint graphs.

k-edge-connected graphs
Edge connectivity is k, i.e., every pair ????

1-isomorphic graphs(Figure 8)
- Graphs whose blocks are isomorphic to one-another
- Isomorphic drarrow 1-isomorphic

2-isomorphic graphs(Figure 9)
Graphs whose blocks(formed by disconnecting two vertices are isomorphic to one-another are said to be 2-isomorphic to each other.
Graphs which are isomorphic to each other by the 2 vertex operation

Circuit correspondence of graphs
- Two graphs have circuit correspondence
  - when there is a one-to-one correspondence between the edges in the graphs and
  - when there is a one-to-one correspondence between the circuits of the graphs such that the circuits formed in one graph with certain edges has a corresponding circuit in the other graph with the same corresponding edges.
- Note that edges in the circuits may be differently ordered.
- Isomorphic, 1-isomorphic and 2-isomorphic graphs have circuit correspondence.

Maximum flow possible b/w 2 vertices in a networks???
Minimum of all the cut-sets between those values.

Removal of a vertex from a graph with n vertices and k components results in between k – 1 and n – 1 components
- In the worst case number of components would be k−1 if the vertex removed was a component in itself.
- For the best case, removal of a vertex from a component might divide the component into deg(v) (if the vertex is a kind of a cut-vertex of the component), making the total number of components equal to n – 1.

If a graph is connected, nothing can be said about the connectedness of its complement

To do
- Deo,
  - Chapter 4 exercises
  - Theorem 4-4