Homogeneous and Non-Homogeneous Linear Systems

Homogeneous linear systems
- A system of linear equations is said to be homogeneous if it can be written in the form Ax = 0, where A is an m times n matrix and 0 is the zero vector in setR^m .
- Such a system always has atleast one solution, namely x = 0, which is called the trivial solution.
- Consider a homogeneous system which has other nontrivial solutions apart from the trivial one. This means that the system does not have just one unique solution. This is possible only if the solution set has atleast one free variable. Thus a homogeneous system has other nontrivial solutions if and only if the it has atleast one free variable. The nontrivial solutions are one per assignment of the free variables.
- When a homogeneous system has other nontrivial solutions, the system has free variable and the solutions sets are in parametric form. The parametric form of the solution set can be expressed as a span of vectors, Span left lbrace bold v_1 , … , bold v_n right rbrace , for suitable vectors bold v_1 , … , bold v_n
  Illustration:
  Consider the simple system, 10x_1 – 3x_2 – 2x_3 = 0
  There is no need for matrix notation. The general solution is x_1 = 3x_2 + 2x_3
  As a vector, the general solution is
  bold x = left [ matrix { x_1 ## x_2 ## x_3 } right ] = left [ matrix {3x_2 + 2x_3 ## x_2 ## x_3 }right ] = left [ matrix {3x_2 ## x_2 ## 0 }right ] + left [ matrix {2x_3 ## 0 ## x_3 }right ] = x_2 left [ matrix {3 ## 1 ## 0 }right ] + x_3 left [ matrix {2 ## 0 ## 1 }right ] = x_2 bold u + x_3 bold v
  Thus every solution of 10x_1 – 3x_2 – 2x_3 = 0 is a linear combination of the vectors u and v. This implies the solution set of 10x_1 – 3x_2 – 2x_3 = 0 is nitalic {Span left lbrace bold u, bold v right rbrace}
- Whenever a solution set is described explicitly with vectors and parameters as above, we say that the solution set is in parametric vector form.
  - When a homogeneous system has one free variable the solution set is of the form tv, where t is the free variable.
  - When a homogeneous system has two free variable the solution set is of the form cv + du, where c and d are free variables.
  - And so on...
- Geometric interpretation
  - The solution set bold x in setR^3= left [ matrix {x_1 ## x_2 ## x_3}right ] = left [ matrix { c_1 x_3 ## c_2 x_3 ## x_3}right ] = x_3 left [ matrix {c_1 ## c_2 ## 1}right ] can be seen as a span of a set of one vector, left [ matrix {c_1 ## c_2## 1}right ] ,if it has one free variable, x_3 . This represents a line through the origin in the 3-dimensional coordinate system.
  - The solution set bold x in setR^3 can be seen as a span of a set of two vectors, nitalic Span\{bold u , bold v \} , if it has two free variables. This represents a plane through the origin in the 3-dimensional coordinate system.
  - A plane through the origin provides a good mental image for the solution set of Ax = 0 even when there are m ore than two free variables.

Non-Homogenous Linear Systems
- Suppose the equation Ax = b is consistent for some given b, and let p be a solution. Then the solution set of Ax = b is the set of all vectors of the form bold nitalic { x = p + v_h } , where bold nitalic v_h is any solution of the homogeneous equation Ax = 0.
  Verification: Ax = A(p + bold v_h ) = Ap + A bold v_h = b + 0 = b
- Geometric interpretation in a three variable system
  - One free variable(Figure ???)
    - In a non-homogenous system, Ax = b with one free variable t, the solution, x = p + tv, can be seen as spanning a line through p in a direction parallel to the line through v and 0. The effect of adding p to some tv is to move this tv in a direction parallel to the line through p and 0. We say that tv is translated by p to tv + p.
  - Two free variable(Figure ???)
    - In a homogenous system, Ax = b, with two free variables c and d, the solution, x = p + cv + du where c and d are the scalars/parameters/free-variables, can be seen as spanning a plane through p parallel to the plane through 0, v and u in the appropriate dimensional coordinate system.
- Even in systems where the number of variables is greater than three, the mental image of the solution set of a consistent system x = b(with bold nitalic {b neq 0} ) is either a single nonzero point of a line or plane not passing through the origin.