Growth of functions

How can the running time of an algorithm be quantified mathematically?
By a polynomial function on the input size, say n.
f(n) = sum from i = 0 to k c_i x^i

What does order of growth of an algorithm talk about?
- It talks about how the running time of an algorithm grows with increase in input size of the problem the algorithm is solving
- The highest order term of the equation representing the running time of the algorithm is representative of the effect of the whole equation. This is because, for large n, the highest order term contributes significantly more to the running time compared to the other terms, to the extent of masking the contributions of the other lower order terms.
- The order of growth thus uses/refers to only the highest order term and ignores the lower order term
- Also the co-efficients of the highest order terms only suggest a constant variation from the highest term itself and are hence also ignored

Definition : Asymptote
Asymptote means equivalent

Asymptotic notation
- Provides us with tools to specify the bounds of the order of growth in the running time of algorithms.
- By bounds, it is meant to specify the boundaries w.r.t which the running time will vary.

Set like conventions of the asymptotic notations
- The below two properties mentioned w.r.t. %THETA function applies to the O, %OMEGA, o, %omega notations as well
  - %THETA of a given function, g(n), is a set of functions specified by %THETA(g(n)) , for a given function, g(n).
  - f(n) = %THETA(g(n)) means f(n) in %THETA(g(n)) .

%THETA notation - %THETA of a given function, g(n)
- Helps specify a a tight(upper and lower) asymptotic bound within which the running time of an algorithm(with a specific type of input actually) varies.
- Graphically, the curve of all f(n) in %THETA(g(n)) always lies between c1g(n) and c2g(n), inclusive, for all n %UxE128 n0
- The running time of an algorithm when described using the %THETA notation does not indicate the running time on every possible type of input, but rather on a particular type of input.
  - Example : Running time of insertion sort is %THETA(n^2) does not imply a tight bound of %THETA(n^2) on every type of input, as insertion sort runs in %THETA(n) on arrays which are already sorted.
- While determining a polynomial representing the running time of an algorithm belonging to a %THETA(g(n)) , a suitable c1, c2, and n0 must be found. Setting c1 to a value that is slightly smaller than the coefficient of the highest-order term of f(n) and setting c2 to a value that is slightly larger permits the inequalities in the definition of %THETA notation to be satisfied.

O notation – O of a given function, g(n)
- Helps specify an upper bound for the order of growth of a function
- The running time of an algorithm when described using the O notation indicates the worst case running time of an algorithm.
- Graphically, the curve of all f(n) in O(g(n)) always lies below cg(n), inclusive, for all n %UxE128 n0

%OMEGA notation - %OMEGA of a given function, g(n)
- Helps specify a lower bound for the order of growth of a function
- The running time of an algorithm when described using the %OMEGA notation indicates the best case running time of the algorithm.
- Graphically, the curve of all f(n) in %OMEGA(g(n)) always lies above cg(n), inclusive, for all n %UxE128 n0

o notation – o of a given function, g(n)
- Helps specify a asymptotic upper bound that is not tight on the growth of a function.
- Graphically, the curve of all f(n) in o(g(n)) always lies below cg(n), exclusive, for all n %UxE128 n0

%omega notation – %omega of a given function, g(n)
- Helps specify a asymptotic upper bound that is not tight on the growth of a function.
- Graphically, the curve of all f(n) in %omega(g(n)) always lies above cg(n), exclusive, for all n %UxE128 n0

Asymptotic notations(AN) in equalities and inequalities
- AN is use on the RHS(only) of an equation and is not a part of a complex formula on the RHS
  - Interpretation - The function on the LHS is a member of the set represented by the F-AN on the RHS
- In general when it appears in an equation it stands for some anonymous function which we do not care to name.
- AN appears in the LHS of an equation
  - Interpretation – No matter what function the AN on the LHS represents, a AN on the right side can be replaced with a suitable function to satisfy the equality.

When is a function asymptotically non-negative?
A function, f(n), is asymptotically non-negative if f(n) is non-negative whenever n is sufficiently large.

Properties of asymptotic notation
- Transitivity
  - f(n) = %THETA(g(n)) and g(n) = %THETA(h(n)) imply f(n) = %THETA(h(n))
  - f(n) = O(g(n)) and g(n) = O(h(n)) imply f(n) = O(h(n))
  - f(n) = %OMEGA(g(n)) and g(n) = %OMEGA(h(n)) imply f(n) = %OMEGA(h(n))
- Reflexivity
  - f(n) = %THETA(f(n))
  - f(n) = O(f(n))
  - f(n) = %OMEGA(f(n))
- Symmetry
  - f(n) = %THETA(g(n)) if and only if g(n) = %THETA(f(n))
- Transpose symmetry
  - f(n) = O(g(n)) if and only if g(n) = %OMEGA(f(n))
  - f(n) = o(g(n)) if and only if g(n) = %omega(f(n))
- If f (x) = O(g(x)), and g(x) = O(f (x)), then f (x) = Θ(g(x)).

Analogy between comparisons of asymptotic notation of two functions and comparisons of two real number a and b
- f(n) = %THETA(g(n)) is like a = b
- f(n) = O(g(n)) is like a le b
- f(n) = %OMEGA(g(n)) is like a ge b
- f(n) = o(g(n)) is like a < b
- f(n) = %omega(g(n)) is like a > b

Theorem 1
Let f (n) and g(n) be functions such that
f (n)
= A.
x→∞ g(n)
lim
Then
1. If A = 0, then f (n) = O(g(n)), and f (n) = Θ(g(n)).
2. If A = ∞, then f (n) = Ω(g(n)), and f (n) = Θ(g(n)).
1. If A = 0 is finite, then f (n) = Θ(g(n)).
References
Introduction to Algorithms - 3rd Edition - Cormen, Leiserson, Rivest, Stein